## Slide 1: Introduction to Robotics Course no. 1
Andrei Dumitriu
andrei.dumitriu@fmi.unibuc.ro
Faculty of Mathematics and Computer Science
University of Bucharest

## Slide 2: About the course: details
Grading:
  1p laboratory, course and/or relevant extra-curricular activity
  4p weekly homeworks
  2.5p project 1: matrix game (bomberman, tetris etc)
  2.5p project 2: line follower
  1p: bonus (activities and/or anything extra on the ones above)
  Total: 11p

## Slide 3: Today’s agenda
Arduino - what is it?
Electrical Current
  Voltage, Current and Resistance
  AC vs DC
Electric components
  Voltage Source
  Resistors
  Capacitors
  Diodes
Ohm’s law
Reading a datasheet

## Slide 4: Sense. Analyse. Act.

## Slide 5: Sense. Analyse. Act.

## Slide 6: Arduino Uno board

## Slide 7: Arduino Uno board on a breadboard
https://www.arduino.cc/en/main/standalone
https://www.sciencebuddies.org/science-fair-projects/references/how-to-use-a-breadboard

## Slide 8: This is a microcontroller (AVR ATmega328)

## Slide 9: But what’s a microcontroller?
An integrated circuit
Basically a tiny computer
Can run small, simple software programs
Low power enough to be run on simple batteries for days
Fast enough to process data efficiently
A typical microcontroller includes a processor, memory and input/output (I/O) peripherals on a single chip

## Slide 10: WARNING
We will work with the HIGH-LEVEL concepts and integrated circuits.
It is not our purpose to design IC, but to understand:
how to select an IC
how to connect an IC
how to understand its limits
how to use its capabilities

## Slide 12: Electric Current
Before you understanding those, though, you need to understand the fundamentals, starting with the electrical current.
Electric circuit: a closed loop that carries electricity.
Picture on the right is correct, but what’s wrong
with it?
https://www.youtube.com/watch?v=gYvXIv7Sj3s

## Slide 13: Electric circuit
Before you understanding those, though, you need to understand the fundamentals, starting with the electrical current.
Electric circuit: a closed loop that carries electricity.
Picture on the right is correct, but what’s wrong
with it?
In a circuit like this there is no resistance, which can
cause overheat and even fire.
Usually there is a consumer in the circuit.

## Slide 14: Current, Voltage and Resistance

## Slide 15: Electric Current
Electric current: flow of electrons in a circuit.
It is the movement, do not confuse it with voltage.
Some analogies include a water current that moves the boat or a wind current that pushes the sail.
Why do electrons “jump” from one atom to the other?
Basically, it’s the potential (the voltage) that pushes the electrons. Each ion (positively charged atom) attracts an electron, creating a new ion. We’ll leave some info for diving deeper.
*Source

## Slide 16: Electric Current
Understanding the difference between conventional electric current flow (hole current, because it leaves a “hole” behind) and electron current flow.
Reasons vary from historic decisions and not wanting to have a lot of “-” in our equations.
*Source

## Slide 17: Electric Current
Imagine instead of seeing the electrons (thus, the negative charge) moving from minus to plus, you can say - and it would be mathematically correct - that the positive charge moves from plus to minus.
We will be working with conventional current flow.
*Source

## Slide 18: Electric Current
This is all very basic, yet super important concept. Take a moment to internalize it. All the calculations are done using hole current, even if in reality the electrons are moving from minus to plus.
*Source

## Slide 19: Electric Current
Units = Ampere (Amp, or “A”).
We will be working with milliamps (mA)
Amps is the stuff that kills you.
*Source

## Slide 20: Electric Current
To sum it up:
current in real life is the flow of electrons
in all circuits we’re not gonna talk about that
we’re gonna say that current comes out the positive terminal and that the unit of measure is the ampere.

## Slide 21: Voltage
Do not confuse with current.
Voltage = the “push” that causes current to flow.
You cannot have any current flowing without something to push it.
When you see that “you can be killed by 10000 volts” it’s incorrectly said. The current kills you, the voltage only causes that current.
Think of blowing through a straw. The air movement is the current, the pressure is the voltage. (can you guess which is resistance?)

## Slide 22: Voltage
Do not confuse with current.
Voltage = the “push” that causes current to flow.
Units = Volt (V)
We will be working mostly with 5V, but generally with an interval between 3.3V and 12V.

## Slide 23: Resistance
It opposes the current flow in a circuit.
Think about the straw. What happens if you increase or decrease the diameter?
Units = Ohm (Ω)
We will be working with units from 110 ohms to few thousand ohms

## Slide 24: Current, Voltage and Resistance

## Slide 25: AC/DC
AC - Alternating Current - Current moves back and forth.
The wall sockets that you use have alternating current.
DC - Direct Current - Constant current flow.
All the batteries you used generate direct current. It gives you constant voltage at the source location (in reality, the battery does die down and current gets weaker, but in a snapshot it’s constant).

## Slide 26: AC
The sine wave is the most common waveform for AC, but not the only one.
https://www.youtube.com/watch?v=WhATjUHgzxQ

## Slide 27: DC

## Slide 28: DC

## Slide 29: AC/DC
The choice for AC over DC in households has been due to AC being easier to transport over long distances.
It’s also easier to generate at power plants etc since they generate heat that creates steam and moves a generator. The wind farms work the same.
Exceptions are batteries, that have a chemical reaction, and solar panels. These generate direct current.
We will not be directly using AC in this course.
Q: why isn’t the light flickering in the house since you use AC?

## Slide 30: Open Circuit
An interrupted circuit through which current does not flow.

## Slide 31: Short Circuit
When you have a circuit with a consumer, but inside it a piece of wire accidentally connects to two terminals (parts of the circuit).
What do you think will happen?

## Slide 32: Short Circuit
When you have a circuit with a consumer, but inside it a piece of wire accidentally connects to two terminals (parts of the circuit).
What do you think will happen?
Remember the foam cutter?
It will generate a lot heat.
And maybe stop the current. Why?

## Slide 33: Electrical Components
You might’ve heard of them in random conversations.
We’ll present a few and look at a big picture overview of what they do.

## Slide 34: Electrical Source
Source Voltage or battery.
Most of the information we’ll present is taken from here: https://www.electronics-tutorials.ws/dccircuits/voltage-source.html

## Slide 35: Electrical Source
Source Voltage or battery.

## Slide 36: Electrical Source
Connecting sources.

## Slide 37: Resistor

## Slide 38: Rezistor
https://www.electronics-tutorials.ws/resistor/res_1.html

## Slide 39: Resistors
Electrical components that limit current in a circuit
Their values can be calculated depending on the color bands
There can have, 3, 4, 5 and even 6 color bands, but we’ll mostly be using with 5. We need to use a table for identifying the value of the colors.
  1st band: 1st digit of the value
  2nd band: 2nd digit of the value
  3rd band: 3rd digit of the value
  4th band: multiplier
  5th band: tolerance ---- aka, error
  6th band: temperature coefficient
For this course, we can ignore tolerance and temperature coefficient

## Slide 40: Resistor value

## Slide 41: Resistors
In order to orient them correctly, pay careful attention to the tolerance ring, as it should be farther apart, but this is not always obvious.
For cheap and easy to find resistors, the tolerance ring is often gold (5%, 4 band, E12) or red (2%, 5 band, E96)
What value does this resistor have?

## Slide 42: Resistors
In order to orient them correctly, pay careful attention to the tolerance ring, as it should be farther apart, but this is not always obvious.
For cheap and easy to find resistors, the tolerance ring is often gold (5%, 4 band, E12) or red (2%, 5 band, E96)
A 2260 Ω, 1% precision resistor with 5 color bands (E96 series), from top 2-2-6-1-1; the last two brown bands indicate the multiplier (×10), and the 1% tolerance. The larger gap before the tolerance band is somewhat difficult to distinguish.

## Slide 43: Capacitor (sau condensator electric)
https://www.electronics-tutorials.ws/capacitor/cap_1.html
The capacitor is a component which has the ability or “capacity” to store energy in the form of an electrical charge producing a potential difference (Static Voltage) across its plates, much like a small rechargeable battery.
Has faster discharge rate than a battery.
Ever heard a blitz charging?

## Slide 44: Capacitor (sau condensator electric)
Unit = Farad(F)
1F is a huge value, we will use µF usually
Are used to also absorb noise in a system

## Slide 45: Diode
https://www.electronics-tutorials.ws/diode/diode_1.html
Diodes are basic unidirectional semiconductor devices that will only allow current to flow through them in one direction only, acting more like a one way electrical valve (Forward Biased Condition).
Can you image how such a component would be built?

## Slide 46: Diode
https://www.electronics-tutorials.ws/diode/diode_1.html
Diodes are basic unidirectional semiconductor devices that will only allow current to flow through them in one direction only, acting more like a one way electrical valve, (Forward Biased Condition).
Can you image how such a component would be built?

## Slide 47: Diode
https://www.electronics-tutorials.ws/diode/diode_1.html
Diodes are basic unidirectional semiconductor devices that will only allow current to flow through them in one direction only, acting more like a one way electrical valve (Forward Biased Condition).
Can you image how such a component would be built?

## Slide 48: PN Junction Diode
https://www.electronics-tutorials.ws/diode/diode_3.html
More precisely:

## Slide 49: LED
What does it stand for?

## Slide 50: LED - Light Emitting Diode
A light-emitting diode (LED) is a semiconductor light source that emits light when current flows through it.
Aka a diode that just happens to emit light.
The invention of the blue LED won the nobel prize: https://www.bbc.com/news/science-environment-29518521

## Slide 51: Transistor
Surely you’ve heard of it.
Super important.
Present in pretty much every electrical component.
Most of the technology in the past 50+ years has been made possible by advancing transistors.
It’s hard to overstate their importance.
It can do 2 things:
  Act as an electronic switch with nothing moving inside (main use)
  Act as an amplifier

## Slide 52: Transistor

## Slide 53: Transistor
Take a few million of these and you can do lots of calculations very, very quickly.
You basically have a digital binary system.
They can turn on and off very fast.
Chips progressed by making transistors faster, smaller and putting more on chips (roughly).

## Slide 54: Ohm’s Law
Super simple - super important, serving as a foundation.
We’ve talked about:
  Current being what actually moves in a system.
  Voltage being what pushes and creates movement.
  Resistance being whatever is in the way and trying to slow down the movement.
We are going to look at very simple systems and apply Ohm’s Law.

## Slide 55: Ohm’s Law
V = IR
  V -> Voltage (Romanian: U)
  I -> Current
  R -> Resistance

## Slide 56: Ohm’s Law
Think about it logically. I = V / R
  Increasing the voltage increases the current
  Increasing the resistance decreases the voltage

## Slide 57: Ohm’s Law
Some simple examples
What’s the current here?

## Slide 58: Ohm’s Law
Some simple examples
What’s the current here?
I = V / R -> I = 5V / 2Ω -> I = 2.5 A (quite a lot)

## Slide 59: Ohm’s Law
Practical example: let’s light up an LED. The arduino provides 5V.
What resistor value do we use? R = V / I -> R = V / 20mA

## Slide 60: Ohm’s Law
Practical example: let’s light up an LED. The arduino provides 5V.
First, let’s check the datasheet for the LED: https://learn.adafruit.com/all-about-leds/the-led-datasheet

## Slide 61: Ohm’s Law
We learnt that:
Arduino provides 5V
The LED has a running current of (about) 20mA
The LED has a voltage drop of 1.8V
The formula is: R = V / I (V = 3.2, I = 20mA)
What numbers do we plug in?

## Slide 62: Ohm’s Law
Well, we calculate the “remaining voltage”:
V_remainder = V_in - V_drop

## Slide 63: Ohm’s Law
Well, we calculate the “remaining voltage”:
V_remainder = V_in - V_drop
V_remainder = 5V - 1.8V = 3.2V

## Slide 64: Ohm’s Law
Well, we calculate the “remaining voltage”:
V_remainder = V_in - V_drop
V_remainder = 5V - 1.8V = 3.2V
We know the desired current: 20mA

## Slide 65: Ohm’s Law
Well, we calculate the “remaining voltage”:
V_remainder = V_in - V_drop
V_remainder = 5V - 1.8V = 3.2V
We know the desired current: 20mA
We apply the formula: R = V / I

## Slide 66: Ohm’s Law
Well, we calculate the “remaining voltage”:
V_remainder = V_in - V_drop
V_remainder = 5V - 1.8V = 3.2V
We know the desired current: 20mA
We apply the formula: R = V / I
R = 3.2V / 20mA = 160 Ω
We will use 220 Ω (closest common value) or 330 Ω if we want it dimmer.

## Slide 67: DC - maybe the difference makes more sense now

## Slide 68: Useful Links
Electronics guide: https://www.electronics-tutorials.ws
Simple electronics guide:
  Voltage, Current and Resistance: https://www.youtube.com/watch?v=OGa_b26eK2c
  Overview of Circuit Components: https://www.youtube.com/watch?v=RHpo4wKo8pQ
  Ohm’s Law: https://www.youtube.com/watch?v=lf0lMDZVwTI
Kirchoff’s Law:
  KVL and KCL examples (haven’t watched it, but from the same series)
  KVL: https://www.youtube.com/watch?v=6F_rmZ1nXFQ
Series and parallel circuits (long video)
Super useful channel: Basic electronics tutorials (list)
Resistor before or after LED?
How to use a breadboard
How to calculate correct resistor for LEDs
Detailed overview or resistors (pretty cool video)
Just use google, though. Each year I find resources that are better and better.

## Slide 69
Source

## Slide 70: Attendance check